## Slide 1
SafeGuard: Congestion and Memory-aware Failure Recovery in SD-WAN
Meysam Shojaee*, Miguel Neves‡ and Israat Haque*
*Dalhousie University
‡ UFRGS University
1

## Slide 2
SD-WANs and network failure
1
2
SafeGuard’s model and architecture
3
Results analysis
4
5
Failure recovery challenges
Conclusion
Outline
2

## Slide 3
Large service providers such as Amazon, Facebook, Google, and Microsoft are deploying SDN in their WAN [1]. University, Halifax, Canada
Institute of Informatics, UFRGS, Brazil
3
SDN deployment examples
B4: Google’s private SD-WAN [2]
Network failures are common in wide area networks [3].
80% of the network component failures last from 10 to 100 minutes which leads to intensive packet loss [4].
Notes: B4 connects 33 Google’s data centers across the globe as of January 2018
Network failures severely degrades application performance

## Slide 4
4
Why failure recovery is challenging is SD-WAN?
x
This route is prone to congestion
Providing short backup routes
conflicts with
making a balanced link utilization
TCAMs are well-known to be power-hungry and to have limited capacity [5]
Shortest route failed
Bandwidth capacity of links are limited
The memory of the switches are limited
The route and traffic rate need to be configured in small Traffic Engineering (TE) cycles
Notes: The forwarding rules in a SDN switch are commonly stored in Ternary Content Addressable Memory(TCAM), a specialized type of high-speed memory

## Slide 5
Minimizing the backup route length
Minimizing the maximum link utilization
5
Problem formulation
We formulated the failure recovery problem as a multi-objective MILP optimization problem
Objectives
1
2
Term 1: The length of the backup route
Term 2: The load on each link
Objective function:

## Slide 6
6
Constraints of the designed model
We have considered a number of constrains in our model:
1. Link bandwidth capacity
2. Switch memory capacity
3. Flow satisfaction
It takes more than one hour to solve the model in CPLEX
The model is an MILP problem which is known to be NP-hard
We developed a heuristic to solve it in a reasonable time
Notes: For a topology like Cogent [7], it takes us more than an hour to solve this model on CPLEX

## Slide 7
7
Operation of the heuristic
15 Mbps
10Mbps
The remaining capacity of all links after the allocation of the flows: 20Mbps except link − whose capacity is 5Mbps
from switch to has a demand of 25Mbps
from switch to requires 20Mbps
10Mbps
10Mbps
X
Both flows are affected by the failure
Key ideas of the heuristic:
Assigns the larger flows to the shorter routes first
When get to the memory usage threshold: best-fit strategy is applied
Notes: we start looking for a “best-fit” demand for it, i.e., demands that can be fully satisfied to ensure that smaller flows have access to shorter routes too

## Slide 8
8
Operation of the heuristic
15 Mbps
10Mbps
routes are allocated to with higher demand
10Mbps
X
X
routes are allocated to after
10Mbps
Notes: For a topology like Cogent [7], it takes us more than an hour to solve this model on CPLEX

## Slide 9
9
SafeGuard’s architecture
Input: a traffic matrix, the network topology, and a set of forwarding routes (primary routes)
Produces a primary allocation that will be used for forwarding traffic under normal conditions
SafeGuard then applies the heuristic to augment the primary allocation with backup routes for all flows for each possible single link failure.
Notes: For a topology like Cogent [7], it takes us more than an hour to solve this model on CPLEX
SafeGuard uses the OpenFlow protocol to configure switches for the primary and backup routes and traffic rates.

## Slide 10
10
SafeGuard’s work-flow
Step A: SafeGuard computes and installs all primary tunnels and splitting weights for every flow
Step B: proactively installs backup routes and computes the weights for allocated flows
Step C: When a failure happens:
the failing switch activates the corresponding backup tunnels
sends a message reporting the failure to the network controller
Step D: the network controller adjusts splitting weights for all affected flows at their respective ingress switches.
Notes: For a topology like Cogent [7], it takes us more than an hour to solve this model on CPLEX

## Slide 11
11
Evaluation setup
Implementation:
We implemented a prototype of SafeGuard using the Ryu SDN controller
Each node is implemented as a CpqD switch instance
Link capacities are set to 1 Gbps
Network topologies:
We considered two networks: B4 with 12 nodes and ATT with 25 nodes
Data generation:
We used Iperf tool to generate UDP traffic
We randomly failed a link in the network
https://github.com/Meysam-Sh/SafeGuard
Notes: We benchmark SafeGuard against Sentinel, state-of-the-art failure recovery scheme for SD-WANs Averages of 30 simulation results with 95% confidence interval.

## Slide 12
12
Results
Sentinel: 57% of links are under 80% + load
SafeGuard: 48% of the links are under 80%+ load
SafeGuard results in backup routes around 10% shorter than Sentinel
48%
57%
Notes: Link utilization: the bandwidth usage percentage over the links / The number of flows is fixed at 60 for B4 and 200 for ATT
(around 40%)

## Slide 13
13
Conclusion
We formulated the failure recovery problem as a multi-objective MILP optimization problem.
We implemented a prototype of SafeGuard using the Ryu SDN controller and evaluated it in Mininet.
Our results show that SafeGuard can reduce the number of congested links by up to 50% compared to the state-of-the-art failure recovery scheme.
SDN is widespread in the production networks. The link failures are a common occurrence in SD-WANs.
We designed and developed a heuristic as the problem was NP-hard.
Notes: SafeGuard requires fewer flow rules:

## Slide 14
14
Any Question?
Notes: SafeGuard requires fewer flow rules:

## Slide 15
20
References:
[1] “Software-defined networking: The new norm for networks,” Open Netw. Found., Palo Alto, CA, USA, ONF White Paper, 2012.
[2] Feamster, N., Rexford, J., & Zegura, E. (2014). The road to SDN: an intellectual history of programmable networks. ACM SIGCOMM Computer Communication Review, 44(2), 87-98.
[3] A. Markopoulou, G. Iannaccone, S. Bhattacharyya, C.-N. Chuah, and C. Diot, “Characterization of failures in an IP backbone,” in IEEE International Conference on Computer Communications (INFOCOM). IEEE, 2004
[4] R. Govindan, I. Minei, M. Kallahalla, B. Koley, and A. Vahdat, “Evolve or Die: High-availability design principles drawn from googles network infrastructure,” in Proceedings of the 2016 ACM SIGCOMM Conference, ser. SIGCOMM ’16, 2016, pp. 58–72
[5] Mohan, P. M., Truong-Huu, T., & Gurusamy, M. (2015, December). TCAM-aware local rerouting for fast and efficient failure recovery in software defined networks. In 2015 IEEE Global Communications Conference (GLOBECOM) (pp. 1-6). IEEE.
[6] Li, J., Hyun, J., Yoo, J. H., Baik, S., & Hong, J. W. K. (2014, May). Scalable failover method for data center networks using OpenFlow. In 2014 IEEE Network Operations and Management Symposium (NOMS) (pp. 1-6). IEEE.
[7] https://cogentco.com/en/network/network-map
Notes: SafeGuard requires fewer flow rules: