## Slide 1: Calibration and Automation of a 5G Simulator for Realistic Evaluation and Data Generation
Conrado Boeira, Antor Hasan, Khaleda Papry, Yue Ju, Zhongwen Zhu, Israat Haque

## Slide 2: Outline
5G Context
Motivation and Research Goals
Calibration Methodology and Results
Automation Tool
Demo
Conclusions
27 June 2024
Notes: we have access to huge volume of data
5G architecture is complex
automation can reduce human error, opex and capex
Hard to directly utilize the actual deployment for testing

## Slide 3: 5G Deployment and Benefits
5G is already widely deployed
Supports emerging applications
  Self-driving cars
  AR/VR
  Mobile gaming
Exponential traffic growth leads to more data-driven solutions
  Automatic solutions reduce OPEX/CAPEX and human errors while offer fast responses
27 June 2024

## Slide 4: Challenges in 5G Innovations
Complex architecture
  Hard to configure and manage
Operators must test new functionalities with appropriate tunned parameters
  Hard to test deployment feasibility
Hard to acquire data for data-driven solutions
  Industries may not share their data due to business interests and privacy
  Researchers may not have access to testbeds
27 June 2024
Notes: we have access to huge volume of data
5G architecture is complex
automation can reduce human error, opex and capex
Hard to directly utilize the actual deployment for testing

## Slide 5: What are the Alternatives?
We can use simulators to test new 5G functionalities
  Allow for fast prototyping of ideas
  Solves the lack of specialized datasets (e.g., anomalies)
Simulators must be trustworthy
They must be efficient to configure and use
27 June 2024
Notes: we can generate anomalies as providers may not label failures, keep them for further analysis, or make it public [1]

## Slide 6: Research Objectives
Realistic and trustworthy simulation
    Calibrate a simulator, Simu5G, to meet 3GPP standards
Learning curve reduction
    Automate Simu5G configuration for better usability
    Develop an automation tool for automatic configuration
27 June 2024

## Slide 7: Why Simu5G?
Open source vs. proprietary simulators
  5G-Lena [2], Simu5G [4] vs. WISE [3], NetSim [5]
Calibrated vs. uncalibrated
  5G-Lena vs. Simu5G
Limitations of 5G-Lena:
  Missing functionalities, e.g., handover
  Do not support dual-connectivity
Simu5G:
  Full stack simulator instead of focusing on a specific layer
  Supports handover, dual-connectivity
27 June 2024

## Slide 8: Methodology
3GPP created a standard scenario for calibrating and comparing simulators [6]
  Each scenario has a predefined set of parameters
Recommend using the following two KPIs as calibration knobs
  Coupling Gain: Difference between the signal strength at the source and destination of a communicating pair
  Wideband SINR: Signal strength to noise plus interference ratio
27 June 2024
Fine tune the simulator to match with 3GPP standards
  Calibrated parameters that not defined by 3GPP
  Performed an exhaustive search through the parameters to achieve the best result

## Slide 9: Implementation
Implemented a couple of use cases (e.g., eMBB-Urban and eMBB-Rural) for the calibration
Implemented the penetration loss and band usage following standards
Implemented the calibration KPIs (coupling gain, Wideband SINR) and their collection interface
Set relevant parameters following 3GPP, including missing ones
  Thermal noise
  User to base station distance
  Building height
27 June 2024

## Slide 10: Evaluation Scenarios and Metric
Urban
  Simulate a dense urban area
  Shorter distance between gNBs (200m)
  3GPP defined Urban path loss model
Rural
  Simulate a sparse rural area
  Larger distances between gNBs (1732m)
  3GPP defined Rural path loss model
Metric: we calculate the CDF of coupling gain and SINR and compare against 3GPP provided CDFs
  3GPP reference submissions include companies like Ericsson, Nokia
27 June 2024

## Slide 11: Results - Urban
In general, we observe a good match on median values
We observe a discrepancy in the lower end values
  It is due to the lack of beamforming in Simu5G
27 June 2024

## Slide 12: Results - Urban
In general, we observe a good match on median values
We observe a discrepancy in the lower end values
  It is due to the lack of beamforming in Simu5G
27 June 2024

## Slide 13: Results - Urban
In general, we observe a good match on median values
We observe a discrepancy in the lower end values
  It is due to the lack of beamforming in Simu5G
27 June 2024

## Slide 14: Results - Rural
Similar behavior as in Urban deployment
27 June 2024

## Slide 15: Results - Rural
Similar behavior as in Urban deployment
27 June 2024

## Slide 16: Results - Rural
Similar behavior as in Urban deployment
27 June 2024

## Slide 17: Results – KS Test
Kolmogorov-Smirinov test attests the closeness of the curves
Similar performance trend as in CDF
27 June 2024
Average discrepancy between Simu5G and 3GPP is below 2 dB
  Within the acceptable range defined by 3GPP
Notes: .g., number of bands, device heights, thermal
noise levels, angle of transmissions, type of penetration losses

## Slide 18: Automating the Simu5G Configuration
Different deployment scenarios require different parameters
  urban, rural, indoor
Requires in-depth knowledge on 5G architectures and protocols
  can be time consuming and error prone
Can we automate the simulator configuration process?
27 June 2024
Notes: .g., number of bands, device heights, thermal
noise levels, angle of transmissions, type of penetration losses

## Slide 19: Automation Tool
We need two types of configurations in Simu5G
  Initialization
    Initial parameters (e.g., transmission power, frequency)
  Network description (NED)
    Topological configurations (e.g., number of devices)
User define high-level configuration information using a YAML file
  Deployment scenarios, number of devices and their locations, KPIs to be collected, etc.
The tool follows 3GPP standards to configure the calibrated Simu5G
27 June 2024

## Slide 20: Results - Automation
1000 lines of code without using the proposed tool vs. ~100 lines with it
27 June 2024

## Slide 21: Demo
27 June 2024

## Slide 22: References
[1] M. Chen, K. Zhu, R. Wang, and D. Niyato, “Active learning-based fault diagnosis in self-organizing cellular networks,” IEEE Communications Letters, vol. 24, no. 8, pp. 1734–1737, 2020.
[2] Koutlia, Katerina, et al. "Calibration of the 5G-LENA system level simulator in 3GPP reference scenarios." Simulation Modelling Practice and Theory 119 (2022): 102580.
[3] Jao, Chin-Kuo, et al. "WiSE: a system-level simulator for 5G mobile networks." IEEE Wireless Communications 25.2 (2018): 4-7.
[4] Nardini, Giovanni, et al. "Simu5G–An OMNeT++ library for end-to-end performance evaluation of 5G networks." IEEE Access 8 (2020): 181176-181191.
[5] www.tetcos.com, “Netsim official developer,” https://www.tetcos.com/, 2018, [Online; accessed 25-March-2024].
[6] ITU-R, “Submission, evaluation process and consensus building for imt-
2020,” ITU-R IMT-2020/2-E, 2019.
[7] L. Rao et al., “5G beamforming techniques for the coverage of intended directions in modern wireless communication: in-depth review,” IJMWT, vol. 13, no. 10, 2021
27 June 2024

## Slide 23: Acknowledgment
27 June 2024

## Slide 24: Concluding Remarks
Calibrated Simu5G following 3GPP guidelines
  To generate trustworthy and accurate data in Urban and Rural deployments
Introduced an API for automated configuration of Simu5G
  Automatic generation of the necessary configuration files based on simpler parameters defined by the user
27 June 2024
Contact:Conrado.boeira@dal.ca

## Slide 25: Evolution of Cellular Communications
Source: https://www.digitalmatter.com/5g-gps-trackers-cellular-iot
27 June 2024
Developments in cellular networks lead to constant innovation
5G is the newest step in this evolution
  Higher bandwitdh
  Lower Latency

## Slide 26: Calibrated Parameters
27 June 2024

## Slide 27: Full Scenario
27 June 2024